## Slide 1: VANET Vehicular Ad Hoc Network
Felix Lu
Month Day, Year

## Slide 2: What is VANET?
Introduction to VANET
FELIX do this page when all 4 papers are done

## Slide 3: Routing in Sparse Vehicular Ad Hoc Wireless Networks
AUTHORS: Nawaporn Wisitpongphan, Fan Bai, Priyantha Mudalige, Varsha Sadekar, and Ozan Tonguz
IEEE Journal on Selected Areas in Communications, Vol. 25, No. 8, October 2007 (pg 1538-1556)

## Slide 4: Points of Discussion
What are the consequences when trying to relay safety messages to other vehicles when the network is constantly disconnected?
In a disconnected VANET what are the key characteristics to observe and what are the adverse effects on performance in the network?
What is the solution to a disconnected VANET if any? And if there is not a viable solution to this problem how can the affects of network fragmentation become minimized?
Given a collection of empirical data, how realistic is it to mathematically model for the scenario of expecting disconnections in a communications network?
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 5: The Car Following Model
Single Lane Model (blue arrows)
  Inter-vehicle distances measured between cars in the same lane
Multi Lane Model (red arrows)
  Inter-vehicle distances measured between the closest adjacent vehicle, which more closely represents the situation of a communications network
  One adjustment from the traditional Car Following Model
Routing in Sparse Vehicular Ad Hoc Wireless Networks
Notes: It is not relevant whether a car is in the same lane, but whether they are within the range of communication

## Slide 6: The Car Following Model
Original Car Following Model
Modified Car Following Model
 | S’ - headway spacing between rear bumper to rear bumper L - effective vehicle length in meters - driver reaction time in seconds V - vehicle sped in meters/second - reciprocal of twice the max average deceleration of a following vehicle (ie approximately 0.075 )
 | - road level inter-vehicle spacing - minimum spacing between any two adjacent vehicles - inter-arrival time of vehicles on any lane from fix observation point V - vehicle sped in meters/second
Routing in Sparse Vehicular Ad Hoc Wireless Networks
Notes: Basis of original model is empirical data gathered by Berkeley Highway Laboratory. However instead of driver reaction time we replace it with inter-arrival time of vehicles into the network. The modified equation then becomes the following: (second)

## Slide 7: Berkeley Highway Laboratory (BHL) Empirical Data
Volume of cars entering network given time of day
Recordings taken at 60 readings/sec
Can be used to extract the inter-arrival times
Peak of traffic volume ~3-5pm
Valley of traffic volume ~1-3am
Vehicle speed (mph) given time of day
Rush hour traffic ~3-5pm
  Causes slower speeds
Routing in Sparse Vehicular Ad Hoc Wireless Networks
Notes: (1)

## Slide 8: Probability Density Function (PDF) of Inter-Arrival Times and Vehicle Speeds
Since we are concerned with disconnected networks, will focus on the 1-3am data (The blue colored lines)
PDF of Inter-arrival time similar to the general exponential distribution
Inter-arrival times range anywhere from 0 to past 30 seconds
PDF of vehicle speeds similar to a normal distribution
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 9: Inter-Vehicle Spacing
Can approximate S = V, which results in figure 5(a)
Inter-vehicle spacing is anywhere from 0 to 1000km!
Can model PDF of inter-vehicle spacing by where
Integrating we can get the Cumulative Density Function of the inter-vehicle spacing.
Define range of communication to be 250m or less
From figure 5(b) we see there is a 65% chance of being connected to the network.
However, this assumes 100% market penetration… Highly unlikely!
Modified Equation for the Inter-Vehicle Spacing:
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 10: Inter-Vehicle Spacing Distribution
This breaks down when the volume is greater than 1000 vehicles/hour, but we are emphasizing the time frame from 1-3am with a sparse traffic density to model a fragmented network.
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 11: Kolmogorov-Smirnov Test (K-S Test)
Tests the goodness-of-fit of the derived models against the empirical data.
Defined by:
For times 1-3am, the D statistic is accurate up to 3%.
For the other time frames, 10am-12pm and 3pm-5pm, the model breaks down and the D statistic is as high as 10%.
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 12: Kolmogorov-Smirnov Test (K-S Test)
Solid and dashed blue lines: 1-3am time frame
The derived model is a good fit to the empirical data for this time frame
The D statistic is at most 3% for this case
The other 2 time frames do not fit as well
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 13: Analytical Data for D Statistics from Kolmogorov-Smirnov Test
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 14: Key Characteristics
Probability of being the last vehicle in a cluster
Average Intra-Cluster Spacing
Average Inter-Cluster Spacing
Average Cluster Size
Average Cluster Length
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 15: Disconnected networks with two directional traffic
Can utilize opposite direction traffic to bridge a network, however will have to incur additional temporal delay
Immediate goal is to broadcast a message from “Src” to “Dst”`
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 16: Spatial Delay
Routing in Sparse Vehicular Ad Hoc Wireless Networks
The delay incurred by broadcasting to vehicles in immediate range is Spatial Relay

## Slide 17: Store-Carry-Forward
Routing in Sparse Vehicular Ad Hoc Wireless Networks
Store-carry-forward referred to as Temporal Relay
Incurs greater temporal delay

## Slide 18: Simulation Results
Simulated results match extremely well with analytical results for both cases of one and two direction probability of being disconnected
Comparing with the empirical results at 1-3am, which showed an approximate volume of 500 veh/hr, the probability of being disconnected is again 35%
The results also show that as traffic density increases, the disconnection probability decreases. This follows reason because it increases the likelihood of vehicles being in the range of R=250m.
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 19: Simulation Results
Analytical and simulated results are nearly identical
As traffic volume increases, the distance between vehicles decreases. This reduces the inter and intra-vehicle spacing as expected.
As more vehicles enter the network, the results also show as expected that the average number of vehicles in a cluster increases. Intuitively, as cluster size increases, it should follow that cluster lengths also increase.
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 20: Simulation Results
The average re-healing time is shown to be impacted by a vehicles speed. It is shown that the re-healing time is dependent on the speed of both east and westbound vehicles. An increase in speed decreases the delay to store and forward messages.
We can also see that an increase in network density decreases the re-healing time. With more vehicles in range of the 250m constraint, the greater amount of spatial relays that can occur to relay messages. Spatial relays are negligible compared to temporal relays therefore significantly reducing the average re-healing times
Routing in Sparse Vehicular Ad Hoc Wireless Networks

## Slide 21: Vehicular Mobility Simulation for VANETs
Authors: Marco Fiore, Jerome Hrri, Fethi Filali, Christian Bonnet
Simulation Symposium, 2007. ANSS ’07. 40th Annual

## Slide 22: VanetMobiSim
There’s no arguing that wireless technology is infiltrating the vehicles we drive everyday. The possibilities are endless, however a common road block in testing prototypes and protocols lies with the resources needed (amount of vehicles) and the large scale of developed roads.
A viable solution is in the realm of simulation. However, a simulation is only as good as it’s ability to properly characterize reality.
One such tool is VanetMobiSim which allows a user to characterize criteria that influence traffic flow
Vehicular Mobility Simulation for VANETs

## Slide 23: Realistic Simulations
Many simulation models do not factor in all the nuances that shape traffic congestion
Traffic conditions are composed of more than just the road lengths, speed limits, and number of lanes. Characteristics of roads such as stop signs versus stop lights at intersections, the proximity to frequented buildings, and characteristics of individual drivers also shape how traffic is formed
VanetMobiSim offers the ability to take into account physical characteristics of road environments as well as characteristics of drivers to properly simulate traffic conditions given a road topology.
Vehicular Mobility Simulation for VANETs

## Slide 24: Macro-Mobility Features
Macro-Mobility features refer to physical characteristics that could possibly affect traffic conditions. Some examples are the number of lanes on a road, traffic signs, speed limits, paths traveled, and of course road topologies.
VanetMobiSim allows the user to customize all these characteristics which is very important because obviously the physical limitations of the driving conditions have an affect on traffic.
Customizable road topologies is another option of VanetMobiSim that allows for realistic simulations. By having this feature a user can model an environment the size of a city, which is a major roadblock to real world testing.
Vehicular Mobility Simulation for VANETs

## Slide 25: Macro-Mobility Features: Road Topologies
User-defined graph: The user lists the vertices and connections to create the graph
GDF map: Geographical Data File. Most of these are not free 
Vehicular Mobility Simulation for VANETs

## Slide 26: Macro-Mobility Features: Road Topologies
TIGER map: road topologies taken from the TIGER database. This is a free source, however the granularity of detail is not as high as with a GDF.
Clustered Voronoi graph: A random generation via a Voronoi tessellation given a set of points. Has ability to vary traffic densities.
Vehicular Mobility Simulation for VANETs

## Slide 27: Macro-Mobility Features: Enhancements
VanetMobiSim offers the following enhancements from CanuMobiSim, in which it was derived
  Ability to model traffic given multiple lanes and directions
  Road dividers separating traffic flowing in opposite directions
  Varying speed limits for different roads given the topology
  Ability to have different traffic flow control mechanisms such as stop signs or traffic lights at intersections. Along with this, the user can also moderate the time in which traffic lights change.
Vehicular Mobility Simulation for VANETs

## Slide 28: Macro-Mobility Features: Movement Patterns
One important aspect of traffic modeling is applying movement patterns to vehicles. In the model, essentially a graph, the movement patterns will dictate how each vehicle moves from vertices to vertices along the edges
  Trip Generation Module: Allows the user to define a set of points of interest so that vehicles follow the given path across specified edges on the graph. This is ideal if we want to force vehicles on a particular path
    Two models associated with the Trip Generation Module
    Random Trip Model: Between a set of points, a random path is decided to reach the destination
    Activity Sequences: The user provides the points of interest and the path to reach the destination
Vehicular Mobility Simulation for VANETs

## Slide 29: Macro-Mobility Features: Movement Patterns
  Path Computation Module: Given a set of points to traverse, the module computes the ideal path to each point. This could be used to model more random traffic as the user is not fully in control of the path vehicles will take
  Three models are included with the Path Computation Module
  Dijkstra’s Algorithm is used by applying a weight to each edge on the graph. As the edge decreases the cost increases
  The weighting can also be determined by the relation between how many vehicles are on the edge. This is used to simulate roads with different densities
  A combination of the two methods with knowledge of the speed limit. This additional knowledge allows the decisions to be based on clearest and fastest path
Vehicular Mobility Simulation for VANETs

## Slide 30: Micro-Mobility Features
Micro-Mobility Features are related to the behavior of individual cars. I believe this is an important
Vehicular Mobility Simulation for VANETs